## Slide 1: EVADC Configuration
  12 bit Resolution by default
  Noise reduction and post calibration disabled for time consumption
  1us Sample time
 | Primary Group |  | Secondary Group | 
Groups & channels | Group 0 | CH0 – CH3 | Group 8 | CH0 – CH15
 | Group 1 | CH4 – CH7 | Group 9 | CH0- CH11, CH14,CH15
 | Group 3 | CH7 | Group 11 | CH0 – CH11
Total Conversion Time | 15+(15*0.3)us |  | 50+(50*0.3)us | 
Broken Wire Detection time for each channel | 300ns |  | 300 ns | 
Interrupt | Last channel of primary queue 0 |  | Last channel of secondary queue 0 | 
iLLD Modification:
A code snippet has added in the iLLD code to enable Broken wire detection

## Slide 2: GTM
TOM |  |  | 
TOM0 | 140Khz (Max) | CH1 – CH3, CH6 – CH14 | Variable phase shift and fixed duty cycle
TOM1 | 60khz (Max) | CH1 – CH6 | Variable duty cycle
TOM2 | 25Khz (TBD) | CH1 – CH4 | Variable duty cycle
TIM |  |  | 
TIM0 | CH5, CH6 | Zero Cross Detection | Interrupt in every raising edge
 | CH1, CH2, CH4, CH7 | Fan Fault Detection | Scanning in every secondary group interrupt

## Slide 3
Tom Global Control Unit, TGC0 drives 0 – 7 channels and TGC1 drives 8 – 15 channels.
As per current hardware pin mapping, few ccx channels falls in TGC0 but their respective coutx channels falls in TGC1. Due to this iLLD limitation, we manually enabled coutx channel register in TGC1.
Cluster-0 clock frequency is 100Mhz but it gives 50 Mhz while retrieving.(need to test and confirm)
We can achieve Phase shift of maximum 90 degree using iLLD. We have manually calculate and write corresponding register (CN0,CM0 – period register and CM1-dutycycle) to achieve phase shift up to 180 deg.
TC377 has only 4 DTM channels for each TOM module. So we used iLLD deadtime for all channels.
CHALLENGES

## Slide 4: GTM starting pulse